## Slide 1: libswitch

## Slide 2: Definitions

## Slide 3: Definitions
Interface
Interface
Channel
Interface
Interface
Channel
Traffic
Ingress Channel
Egress Channel
Governor
(e.g. ACE, Routes…)
Switch
Endpoint

## Slide 4: Interface
The physical representation of ports on a switch.

## Slide 5: Channel
The abstract representation of established communication links on a switch.
Has three types
  direct
  A direct representation of an interface.
  VLAN
  A VLAN channel with designated ID.
  aggregate
  Represent by multiple interfaces, e.g. port channel.
Maintain a list of endpoints.

## Slide 6: Traffic
Describe the relationships between channels.
Compose of three attributes
  ingress
  Describe the input channel of this traffic.
  egress
  Describe the output channel of this traffic.
  governor
  The statistics and rules between ingress and egress.
  e.g. ACE, subnet of the routing rule

## Slide 7: Endpoint
An endpoint connects to the interface of a switch.
It can be either an unknown device, or a switch that hasn’t been identified.
Has two must-have attributes
  MAC address
  IP address

## Slide 8: Switch
A switch is an identified endpoint.
Has one attribute
  brand
  The manufacturer, which decides the command set.
  protocol
  The way this switch establish connection right now.
  i.e. RS232, SSH or HTTPS.
Contain list of interfaces, channels and traffics.

## Slide 9: Command Set

## Slide 10: Overview
All the brands share a common command set, but the implementation differs by manufacturers and the protocols.